## Slide 1: Logical Operations
Microprocessor and Assembly Programming Laboratory
CSC214A
Laboratory 3

## Slide 2: Theoretical Background
Instruction | Explanation
andb $10, %al | ands the immediate value 10 to the 8-bit AL register
andw %bx, %cx | ands the 16-bit value of the BX register to the CX register
andl data, %eax | ands the 32-bit integer value at the data label to EAX
andl %eax, %eax | ands the value of the EAX register to itself

## Slide 3: Theoretical Background
The following Boolean logic operations are provided:
          AND
          NOT
          OR
          XOR
The AND, OR, and XOR instructions use the same format:
and source, destination

## Slide 4: Aim
To develop assembly language program to perform all logical operations

## Slide 5: Expected Outcomes
At the end of this lab students will be able to
  Identify the appropriate assembly language instruction for the given logical operations
  Perform all logical operations using assembly language instructions
  Get familiar with assembly language program by developing simple programs

## Slide 6: Example
movb $20, %al
andb $10, %al
movsx %al, %eax
movw $100, %cx
andw %cx, %bx
movsx %bx, %ebx
movl $100, %edx
andl %edx, %edx
andl data, %eax
andl %eax, data
movl $1, %eax
movl $0, %ebx
int $0x80
andtest1.s - An example of the AND instruction
.section .data
data:
.int 40
.section .text
.globl _start
_start:
nop
  movl $0, %eax
  movl $0, %ebx
  movl $0, %ecx

## Slide 7: Expected Output
(gdb) print $eax
$1 =
(gdb) print $ebx
$2 =
(gdb) print $ecx
$3 =
(gdb) print $edx
$4 =
(gdb) x/d &data
0x804909c <data>:
(gdb)

## Slide 8: Expected Documentation Detail
Algorithm
  Write and explain the logical instructions to perform all the given assignment statements
Presentation of Results
  Present the screenshots with explanation
    Refer Expected output slide
Analysis and Discussions
  Compare your experience on Assembly language programming with C programming language and discuss the differences
    Assembly language is a low level language and dependent on the system architecture but in case of C, it can be ported to various platforms

## Slide 9: Expected Documentation Detail
Conclusions
  Based on your work and analysis provide a summary and conclusions drawn from the analysis here
    The assembly code for one architecture can not port to another architecture with out radical rewrite of the code
Comments
  Limitations of Experiments
    Is the experiment and the delivery in lab session complete to achieve the objectives? What else can be done to improve the experiment.

## Slide 10: Expected Documentation Detail
Comments
  Limitations of Results
    Are the results of the experiment restricted? How can they be overcome
  Learning happened
    What did you learn
  Recommendation
    Based on your understanding and analysis, what do you recommend. Do you have any recommendations to overcome limitations of the experiment?