## Slide 1: Array Manipulation
Microprocessor and Assembly Programming Laboratory
CSC214A
Laboratory 4

## Slide 2: Theoretical Background
Using indexed memory locations
values:
.int 10, 15, 20, 25, 30, 35, 40, 45, 50, 55, 60
The way this is done is called indexed memory mode. The memory location is determined by the following:
  A base address
  An offset address to add to the base address
  The size of the data element
  An index to determine which data element to select

## Slide 3: Theoretical Background
The format of the expression is
  base_address(offset_address, index, size)
The data value retrieved is located at
  base_address + offset_address + index * size
    movl $2, %edi
    movl values(, %edi, 4), %eax

## Slide 4: Theoretical Background
Using indirect addressing with registers
While using a label references the data value contained in the memory location, can get the memory location address of the data value by placing a dollar sign ($) in front of the label in the instruction. Thus the instruction
      movl $values, %edi
is used to move the memory address the values label references to the EDI register.

## Slide 5: Theoretical Background
.section .data
values:
.int 10, 15, 20, 25, 30, 35, 40, 45, 50, 55, 60
.section .text
.globl _start
_start:
nop
movl values, %eax
movl $values, %edi
movl $100, 4(%edi)
movl $1, %edi
movl values(, %edi, 4), %ebx
movl $1, %eax
int $0x80

## Slide 6: Aim
To develop assembly language program to access the elements in an array or to access a particular element in an array using indexed addressing mode

## Slide 7: Expected Outcomes
At the end of this lab students will be able to
  Perform array manipulation using indexed addressing mode
  Discuss indexed addressing modes
  Access the appropriate element in an array

## Slide 8: Example
.section .data
output:
.asciz “The value is %d\n”
values:
.int 10, 15, 20, 25, 30, 35, 40, 45, 50, 55, 60
.section .text
.globl _start
_start:
nop
movl $0, %edi
loop:

## Slide 9: Example
movl values(, %edi, 4), %eax
pushl %eax
pushl $output
call printf
addl $8, %esp
inc %edi
cmpl $11, %edi
jne loop
movl $0, %ebx
movl $1, %eax
int $0x80

## Slide 10: Expected Output
$ as -o movtest3.o movtest3.s
$ ld -dynamic-linker /lib/ld-linux.so.2 -lc -o movtest3 movtest3.o
$ ./movtest3
The value is 10
The value is 15
The value is 20
The value is 25
The value is 30
The value is 35
The value is 40
The value is 45
The value is 50
The value is 55
The value is 60

## Slide 11: Expected Documentation Detail
Algorithm
  Write and explain algorithm to perform the given array manipulation
Presentation of Results
  Present the screenshots with explanation
    Refer Expected output slide
Analysis and Discussions
  Compare your experience on Assembly language programming with C programming language and discuss the differences
    Assembly language is a low level language and dependent on the system architecture but in case of C, it can be ported to various platforms

## Slide 12: Expected Documentation Detail
Conclusions
  Based on your work and analysis provide a summary and conclusions drawn from the analysis here
    The assembly code for one architecture can not port to another architecture with out radical rewrite of the code
Comments
  Limitations of Experiments
    Is the experiment and the delivery in lab session complete to achieve the objectives? What else can be done to improve the experiment.

## Slide 13: Expected Documentation Detail
Comments
  Limitations of Results
    Are the results of the experiment restricted? How can they be overcome
  Learning happened
    What did you learn
  Recommendation
    Based on your understanding and analysis, what do you recommend. Do you have any recommendations to overcome limitations of the experiment?